## Slide 1
Tran, Viet Cuong
Department of Electronics Engineering, Keimyung University
Daegu, Korea
25th October 2017
Smart Wearable Controlling System by Hand and Finger Gestures

## Slide 2: Content
  Introduction
  System Design
  Method
  Experiments and Results
  Conclusion & Future Work

## Slide 3: Content
Introduction
  Gesture Recognition
  Literature View
  Smart Wearable Controlling System
System Design
Evaluation Result
Conclusion & future work

## Slide 4: Gesture Recognition
Gesture recognition has become on of the popular research fields that served as an intelligent and a natural interface.
Exploring alternative ways to recognize the imitate human gestures to perform complex and difficult tasks in various areas.
Wearable computing trends allowed devices to be portable and smaller in size.

## Slide 5: Literature Review
Vicon system [1] captures the motions by using multiple high-speed infrared cameras
Pathk [2] presented a framework for hand gesture recognition
Gesture control armband using single EMG and IMU

## Slide 6: Smart Wearable Controlling System
Tend to wearable computing trend and high accuracy rate:
Utilizing only three IMUs
Recognizing 22 gestures

## Slide 7: Content
  Introduction
  System Design
    System Overview
    Design of Hardware
    Design of Software
  Method
  Experiments and Results
  Conclusion & future work

## Slide 8: System Overview
The system includes:
Sensor module
Processing module
Mobile device
IMU sensors
IMU Multiplexer
Bluetooth module
Processing Module

## Slide 9: System Overview
System design overview.

## Slide 10: System Overview
Proposed smart wearable controller system can be applied to various applications.
Qt cross platform software
Applying to various applications as home automation, games controller …

## Slide 11: Hardware
(a) Schematic and (b) PCB layer design of sensor module.
(a) Schematic and (b) PCB layer design of processing module.

## Slide 12: Hardware
Appearance design using 3D Printer

## Slide 13: Design of Software
Qt cross-platform application development framework.
Cross-platform application framework (Linux, OS X, Windows, Android, iOS).
Framework written in C++.
GUI is written in QML instead of the whole application whereas the application’s backend is written in C++.

## Slide 14: Design of Software
Screenshot of the smart home application
System overview of smart home application.

## Slide 15: Design of Software
Video Demo

## Slide 16: Content
  Introduction
  System Design
  Method
    Dynamic Time Warping (DTW)
    N Dimension – DTW
    Pre-processing
    Training
    Classification Threshold
  Experiments and Results
  Conclusion & future work

## Slide 17: Method
Flowchart of method

## Slide 18: Dynamic Time Warping (DTW)
DTW is an algorithm that can compute the similarity between two time-series, even if the lengths of the time-series do not match.
Two identical time-series signals, with phase differences measured with (a) Euclidean distance and (b) Dynamic Time Warping.
DTW has been applied to temporal sequences of video, audio, graphics data and gesture recognition.

## Slide 19: Dynamic Time Warping (DTW)
Example of warping path in a distance table. Length of class sequence, x = 6 and length of test sequence, y = 5.
- Given two, one-dimensional, time-series
- Construct a warping path
- A number of constraints are placed on the warping path which are as follows:
start at: w1 = (1, 1)
end at: w|w| = (|x|, |y|)
Continuous
cannot move backwards.
- The warping cost given by:
where is the distance function (Euclidean)

## Slide 20: N Dimension DTW
Multiple dimension DTW
Computing the distance between 2 given time-series.
The total distance across all N dimensions is used to construct the warping matrix with the Euclidean distance:

## Slide 21: Pre-processing
Accelerometer is reliable only in the long run, but so noise in the short run.
Gyroscope is reliable only in the short run, but is drifted in the long run
Using measurement by the fusion of accelerometer and gyroscope data with Complementary filter:

## Slide 22: Training
Template is required to store all the intended gestures in database by recording Mg training samples for each of the G gestures
Each of G template can be found by computing distance each of Mg training samples
Searching for the training samples that provide the minimum warping distances when compare the other training samples in that class

## Slide 23: Classification Threshold
The N-dimensional input time-series X is not matched with any of the gestures in the template
Thus this false classification issue can be resolved by defining a classification threshold for each gesture in the template during the training phase.
The algorithm will indicate the particular gesture as no match:
where d is the total normalized warping distance
could be initially set to any number during the training phase and later be adjusted by the user

## Slide 24: Content
  Introduction
  System Design
  Method
  Experiments and Results
    Experiment Setup
    Results and Discussions
  Conclusion & future work

## Slide 25: Experiment Setup
Six right handed subjects are voluntarily participated in the experiments.
Subjects are requested to perform 25 repetitions of 22 gestures.
The gestures consisted of 18 hand gesture and 4 fingers gestures.
The predefined 18 gestures
Four finger gestures

## Slide 26: Experiment Setup
Orientation samples obtained from 3 IMUs to the gestures including (a) rotate right, (b) rotate left, (c) zoom in and (d) zoom out.
Self-development application for the purposes of training phase and testing phase.

## Slide 27: Result and Discussion
Experiments are conducted to validate the gesture recognition accuracy rate utilizing the ND-DTW algorithm.
The impact to accuracy rate based on the quantity of IMUs used are also taken into consideration.
The ND-DTW model was trained using 6-fold cross validation method

## Slide 28: Result and Discussion

## Slide 29: Content
  Introduction
  System Design
  Method
  Experiments and Results
  Conclusion & future work
    Conclusion
    Future Work

## Slide 30: Conclusion
Focused on the design and implementation of smart wearable controller system using hand and fingers for gesture recognition.
The system utilized 3 IMUs sensors, to recognize total of 22 pre-defined gestures with DTW algorithm with low cost implementation and high accuracy rate.
The study evaluated the IMUs quality impacted to the accuracy rate of system.
System performed well with low energy consumption of 10 hours with 3.7V 240mA battery

## Slide 31: Future Work
Optimization of PCB design in term of size and dimensionality to reduce power consumption and its wearable comfortability.
Implementation of recognition algorithm in embedded hardware as standalone system which is compatible to different software platforms.
Recognition of more complex gestures that involved three dimensional gestures by utilizing hand and fingers motion.
Inclusion of more functionalities for various applications and allow gestures self-customization by users.

## Slide 32
THANK YOU!
UBIQUITOUS SENSOR NETWORK LABORATORY

## Slide 33
Q&A
UBIQUITOUS SENSOR NETWORK LABORATORY

## Slide 34: Reference